## Slide 1: ICLAB Lab05 EXERCISE
0810774 Cheng-Yen lo
2023/04/12

## Slide 2: OUTLINE
Design Consideration
  Data Flow
  FSM States
  Hardware Consideration
Optimization
  Area
  Cycle & Cycle Time
Reference

## Slide 3: Design Consideration

## Slide 4: data flow
Storage:
  Get a matrix size
  Get 32 matrices continuously at the beginning of each pattern
Calculation:
  Get a mode for the transpose matrix
  Get 3 matrices indices for multiplication
  Finishing matrix multiplication & find its trace

## Slide 5: data flow
Trace: sum of the eigenvalues
Multiplication of matrices needs to maintain order
Trace of transpose matrix is equal to original one

## Slide 6: data flow
By commutative law, we can push the transpose one to last one
Row transpose = Column
Matrix B
Matrix C (transpose)
Matrix B * C

## Slide 7: data flow
Matrix B
Matrix C (transpose)
Matrix B * C
Matrix B
Matrix C (transpose)
Matrix B * C

## Slide 8: data flow
Matrix B
Matrix C (transpose)
Matrix B * C
Matrix A
Matrix B * C
Trace

## Slide 9: Hardware Consideration
SRAM:
  8 bits * 8192 word
  128 bits * 512 word
Transpose Storage:
  SRAM: 128bits * 16 * (32+1) words = 128bits * 528 words

## Slide 10: FSM States
IDLE:
  In_valid1 -> Storage
  In_valid2 -> Input
STORAGE: save 32 matrices & size -> IDLE
INPUT: save 3 matrices indices & mode -> WAIT
WAIT:
  Mode = 0 -> TRANS
  Mode = 1,2,3 -> CAL(contain output)
  Mode = 0 & Transpose finish -> CAL(contain output)
TRANS: matrix transpose, finish -> SAVE_TR
SAVE_TR: save transpose matrix to SRAM , finish -> WAIT

## Slide 11: OPtimization

## Slide 12: Area
Matrix B
Matrix C (transpose)
Matrix B * C
Matrix A
Matrix B * C
Trace
20 bits Reg * 16
Column of B*C multiply with Row of A
Need to storage column of Matrix B * C
Need 16 multipliers & 15 adders for matrix A*B*C
Multiplier: 28 bits
Adder: 36bits

## Slide 13: Area
Matrix B
Matrix C (transpose)
Matrix B * C
Matrix A
Matrix B * C
Trace
Pipeline:
  B*C multiply with A
Save storage column of Matrix B * C
  20 bits Reg * 16
Save multipliers & adders
Prepare row of A first (needs to storage it)

## Slide 14: Cycle & Cycle Time
Critical path: DRAM to multipliers to adders(16 to 1, 4levels)
Pipeline:
  Separate multipliers & adders
  DRAM to multipliers: ~5ns
  Adders (4levels): ~4ns
Transpose 2 rows same time
  Save ½ cycles when mode = 0
  Reuse the registers of A’s row storage register

## Slide 15: Reference

## Slide 16
PhD
2de 沒過
OT 沒用IP過了
維尼學長

## Slide 17: Thanks for your listening