## Slide 1: LAB 06 Exercise
2023.04.19
Presenter: Tzu-Yun, Yen

## Slide 2: Outline
Topic Review
Soft IP
  Extended Euclidean Algorithm
  Design
  Optimization
Top Module
  Data Flow Graph
  Optimization

## Slide 3: Topic Review
Given the parameter a of an elliptic curve and two points P and Q on the curve, the task is to find the third point R s.t. P+Q+R=O, where O means an abstract point at infinity (無窮遠點).
All computations should be performed in a specific prime field (Fp).
Since we need to do the division over Fp, we need to find the inverse of the field elements, inverses can be efficiently computed by using the extended Euclidean algorithm (輾轉相除法).

## Slide 4: Topic Review
The design can be derived into two part:
  Soft IP – compute the inverse of the field element.
  Top Module – compute the coordinate of R.

## Slide 5: Soft IP

## Slide 6: Soft IP
The inverse of the field element b with the prime number a is defined as:
The congruence relation may be rewritten as:
We can use Extended Euclidean Algorithm to find the inverse of b. (i.e. the value of y)

## Slide 7: Extended Euclidean Algorithm
Extended Euclidean Algorithm Example
  a = 113, b = 30
  When r = 1, we get x = -13, y = 49 ⇒ inverse = 49
a*x + b*y = 113 * -13 + 30 * 49 = 1

## Slide 8: Verilog Code
compute q, r
compute a, b
compute y
select output

## Slide 9: Problems in Soft IP Design
How many iterations do we need to compute inverter?
  IP_WIDTH = 5 ⇒ 5 iters
  IP_WIDTH = 6 ⇒ 6 iters
  IP_WIDTH = 7 ⇒ 7 iters
How many bits are required for each variable?
  a, b, q, r ⇒ IP_WIDTH bits (unsigned)
  y ⇒ IP_WIDTH + 1 bits (signed)

## Slide 10: Optimization 1
Observation: The sign of y is reversed at each iteration.
Change the calculation of y to
⇒ the bit width of y can be reduced by one. (signed → unsigned)

## Slide 11: Optimization 2
Observation
  The inverse of b is equal to the negative of the inverse of prime - b.
  One more iteration is required if b > prime/2.
Limit the field element b between 1 and prime/2
⇒ the iteration can be reduced by one.

## Slide 12: Optimization 1 & 2
Optimization 2
Optimization 1

## Slide 13: Optimization 3
For IP_WIDTH = 6, set each variable’s bit width separately.
Since the quotient of the 5th iteration can only be 1, actually, we don't need to do the 5th division
⇒ only need 4 dividers(/), 4 remainders(%), 3 multipliers(*) and 5 adders(+)

## Slide 14: After Optimization
How many iterations do we need to compute?
  IP_WIDTH = 5 ⇒ 4 iters
  IP_WIDTH = 6 ⇒ 4 iters (+ 1adder)
  IP_WIDTH = 7 ⇒ 6 iters
How many bits are required for each variable (a, b, q, r, y)?
  for IP_WIDTH = 5 or IP_WIDTH = 7 ⇒ IP_WIDTH bits (unsigned)
  for IP_WIDTH = 6 ⇒ set separately

## Slide 15: Top Module

## Slide 16: Top Module
The elliptic curve over Fp is defined as
The expressions for the group operation over prime field

## Slide 17: Data Flow Graph
The data flow graph is shown as below
compute s
compute Rx
compute Ry

## Slide 18: Pipeline
Theoretically
  pros: cycle time ⇓ & area ⇓ (∵ hardware reuse)
  cons: latency ⇑
Pratically
  Cycle time is limited by the longest data path.
⇒ Too many stage of pipeline will cause pipeline imbalance.
  The smaller cycle time, the larger components that Design Compiler will choose.
  We need extra muxs to select the input of reused hardware.
⇒ The decrease in area is not proportional to the increase in latency.

## Slide 19: Optimization
Strategies
  Divided into 2.5 pipeline stages
  Only reuse one multiplier and one remainder in each pipeline.
clk
in_valid
out_valid
latency = 1
(1)
(2)
(3)

## Slide 20: After Optimization
(1)
(2)
(3)

## Slide 21: The End
Thanks for listening :)

## Slide 22: Data Flow Graph
Py
<<1
-p?
–
Py
Qy
-p?
–
Px
Qx
inv
%
x
Ry
Px
Px
%
+
a
%
x3
x

## Slide 23: Data Flow Graph
+
Px
Qx
%
x
–
-p?
–
%
x
Px
Py
–
-p?
Rx
Ry